## Slide 1
VALUE STREAM MAP — CURRENT STATE (edit every shape; duplicate with Cmd/Ctrl-D)
Value stream: click to type Date: __ / __ / ____ Prepared by: click to type
Supplier
2× weekly
Production Control
Weekly MRP
Customer
18,400 pcs/mo
Takt = available time ÷ demand
Stamping ◉ 1 op
C/T
1 sec
C/O
1 hr
Uptime
85%
Weld ◉ 1 op
C/T
39 sec
C/O
10 min
Uptime
100%
Assembly 1 ◉ 1 op
C/T
62 sec
C/O
—
Uptime
100%
Assembly 2 ◉ 1 op
C/T
40 sec
C/O
—
Uptime
100%
I
5 days
I
7.6 days
I
1.8 days
I
2.7 days
I
4.5 days
2× weekly
1× daily
C/O reduction
5 d
1 sec
7.6 d
39 sec
1.8 d
62 sec
2.7 d
40 sec
4.5 d
waiting (days) ↑ processing (time) ↓
LEAD TIME
21.6 d
PROCESS TIME
2.4 min
VALUE-ADD
0.03%
How to use: replace the example with your own stream — every element is a shape. Duplicate a process box + data box (Cmd/Ctrl-D) to add steps. Slide 2 is a symbol library: copy supermarkets, FIFO lanes, and kaizen bursts from there. Prefer clicking to build it (with the math computed for you)? kaizumi.com/tools/vsm

## Slide 2
VSM SYMBOL LIBRARY — copy these onto your map (Cmd/Ctrl-C → V)
Process ◉ 1 op
C/T
— sec
C/O
—
Uptime
—%
Process + data box
One transformation step. Keep C/T, C/O, uptime honest — walk the floor.
Supplier / Customer
frequency
External source
Sawtooth roof = outside the plant. Put demand or delivery frequency on it.
I
— days
Inventory
Material waiting. Count it, convert to days of demand — the lead-time driver.
Supermarket
Controlled shelf the downstream process pulls from. Pair with a pull arrow.
Push arrow
Material moved on schedule regardless of downstream need.
pull
Pull / withdrawal
Downstream withdraws only what it needs from a supermarket.
FIFO
FIFO lane
Capped first-in-first-out channel — sequence preserved between steps.
kaizen
Kaizen burst
Marks where an improvement is needed to reach the future state.
daily
Truck shipment
External deliveries in or out; label the frequency.
Electronic info
Zigzag = ERP / EDI / email. Straight thin arrow = manual (paper, verbal).
Timeline ladder
High = waiting (days). Low = processing. Totals give lead time and % value-add.
LT / PT / %VA
Totals box
Lead time, process time, and percent value-add — the punchline of the map.
Build it interactively — with takt, lead time, and the bottleneck computed live — at kaizumi.com/tools/vsm